## Slide 1
Monitoring and modelling of POP pollution: main activities and results
Alexey Gusev on behalf of MSC-E and CCC

## Slide 2
Review and improvement of POP emissions data for modelling
Analysis of long-term trends in POP pollution
Monitoring of POP pollution in the EMEP region
Assessment of POP transboundary pollution (regional/global)
Evaluation of PAH pollution of urban areas and selected cities
Scientific co-operation on improvement of model assessment quality
Transition of modelling to the new EMEP grid
Co-operation with subsidiary bodies, international organizations and programmes
Main directions of work in 2016/2017
2016/2017 workplan (ECE/EB.AIR/133/Add.1)

## Slide 3
Development of strategy to improve emissions
Analysis of key parameters of POP emission affecting model assessment
Emission parameters:
Quality of gridded emissions
Chemical composition
Seasonal variations
Vertical distribution
Global emissions
Historical emissions
Emissions to media
Congener composition of PCDD/F emission
0%
5%
10%
15%
20%
TCDF
12PeCDF
23PeCDF
14HxCDF
16HxCDF
23HxCDF
19HxCDF
78HpCDF
89HpCDF
OCDF
TCDD
PeCDD
4HxCDD
6HxCDD
7HxCDD
HpCDD
OCDD
40%

## Slide 4
Development of strategy to improve emissions
Analysis of key parameters of POP emission affecting model assessment
Emission parameters:
Quality of gridded emissions
Chemical composition
Seasonal variations
Vertical distribution
Global emissions
Historical emissions
Emissions to media
Seasonal variation of B[a]P emission from residential heating

## Slide 5
Development of strategy to improve emissions
Analysis of key parameters of POP emission affecting model assessment
Emission parameters:
Quality of gridded emissions
Chemical composition
Seasonal variations
Vertical distribution
Global emissions
Historical emissions
Emissions to media
Contribution to joint CEIP/MSC-E report on the improvement of emission data for modelling
Historical emissions of HCB
0
4000
8000
12000
16000
20000
1945
1949
1953
1957
1961
1965
1969
1973
1977
1981
1985
1989
1993
1997
2001
2005
2009
2013
HCB emissions, t/y
Min
Ave
Max

## Slide 6
Evaluation of long-term trends in POP pollution
Contribution to CLRTAP, WGE and TFMM Assessments-2016
Temporal changes of B[a]P, PCDD/F, PCB, and HCB air concentrations
Analysis of trends for 1990-2012 indicates decrease of B[a]P, PCDD/F, PCB, and HCB air concentrations from about 30% to almost 90%
More significant reduction occurred in first decade (1990-2000)
Slower reduction in second decade (2001-2012), and stabilization of B[a]P air concentrations
30%
45%
80%
90%
0
20
40
60
80
100
1990
1992
1994
1996
1998
2000
2002
2004
2006
2008
2010
2012
Decrease, %
B[a]P
PCDD/Fs
PCB-153
HCB

## Slide 7
Temporal changes of B[a]P air concentrations in the EMEP countries
EU28
0.0
0.1
0.2
0.3
0.4
1990
1992
1994
1996
1998
2000
2002
2004
2006
2008
2010
2012
2014
B[a]P in air, ng/m
3
Value
Trend
Czech Republic
0.0
0.3
0.6
0.9
1990
1992
1994
1996
1998
2000
2002
2004
2006
2008
2010
2012
2014
B[a]P in air, ng/m
3
Value
Trend
Temporal changes of PCB-153 air concentrations in the EMEP countries
Evaluation of long-term trends in POP pollution
Trends of PCB and B[a]P concentrations for 1990-2014
EMEP
0
0.5
1
1.5
2
1990
1992
1994
1996
1998
2000
2002
2004
2006
2008
2010
2012
2014
PCB-153 in air, pg/m
3
Value
Trend
Poland
0
1
2
3
4
5
6
7
1990
1992
1994
1996
1998
2000
2002
2004
2006
2008
2010
2012
2014
PCB-153 in air, pg/m
3
Value
Trend
Main component

## Slide 8
Measurement/Modeling assessment for 2014
Monitoring of PAH, PCB, and HCB concentrations in the EMEP region
Measurements of PAH concentrations were reported by 31 monitoring site
PCBs and HCB were measured at 13 sites
Passive sampling measurements of PCBs from UNEP SC GMP Datawarehouse
No regular measurements of PCDD/F concentrations
B[a]P
HCB
PCB-153

## Slide 9
Measurement/Modeling assessment for 2014
Annual mean modelled PCB-153 air concentrations, 2014
Modelled PCB-153 air concentrations agree with measurements
Variations of PCB-153 air concentrations from 2013 to 2014 amounted to about 30%
Evaluation vs. measurements of EMEP monitoring stations
Evaluation of PCB-153 pollution levels in the EMEP region
0
1
2
3
CZ3
DE1
DE2
DE3
DE8
DE9
FI36
SE12
SE14
NO2
NO42
NO90
PCB-153 in air, pg/m3
Observed
Modelled
Measurement/modelling agreement

## Slide 10
Measurement/Modelling assessment for 2014
Modeling results agree with passive sampling measurements within a factor of 2 – 3
Evaluation vs GMP DWH passive sampling measurements in Europe
Annual mean modelled PCB-153 air concentrations, 2014
Evaluation of PCB-153 pollution levels in the EMEP region
0
1
2
3
4
5
0
1
2
3
4
5
Observed, pg/m3
Modelled, pg/m3
factor 3
factor 2
Measurement/modelling agreement

## Slide 11
Measurement/Modelling assessment for 2014
Annual mean modelled HCB air concentrations, 2014
Measurement/modelling agreement
Evaluation vs. measurements of EMEP monitoring stations for 2012-2014
Evaluation of HCB pollution levels in the EMEP region
Modelled HCB air concentrations agree with EMEP measurements within a factor of 3
The model tend to underestimate measured HCB air concentrations
x3
x3

## Slide 12
Measurement/Modelling Assessment 2014
~70% of modelled concentrations are within a factor of 2 in comparison with measurements of 4PAHs
Annual mean modelled PAH air concentrations, 2014
Evaluation of PAH pollution levels in the EMEP region
Measurement/modelling agreement
Evaluation vs. measurements of EMEP monitoring stations for 2014
x2
x2

## Slide 13
Measurement/Modelling Assessment 2014
Modelled B[a]P concentrations are generally within a factor of 2 in comparison with measurements
Daily variations of B[a]P concentrations
Annual mean modelled and observed B[a]P concentrations
0.0
0.2
0.4
0.6
0.8
PL0005R
DE0002R
DE0009R
CZ0003R
DE0001R
SE0011R
DE0008R
SE0012R
GB0036R
SE0014R
GB0048R
DE0003R
FI0036R
B[a]P in air, ng/ m3
Observed
Modelled
Evaluation of B[a]P pollution levels in the EMEP region

## Slide 14
PAH deposition in 2014
Measurement/Modelling Assessment of PAH pollution, 2014
Transboundary transport of pollution
For about 70% of the countries contribution of transboundary fluxes exceeded contribution of national emissions to deposition
Substantial part of deposition originated from emissions of several countries (the Russian Federation, Ukraine, Kazakhstan, Spain, and Poland)
PAH deposition to EMEP countries
0%
25%
50%
75%
100%
FYR Macedonia
Greece
Belarus
Georgia
Bulgaria
Germany
Albania
Czech Republic
Slovakia
Kyrgizstan
Slovenia
Serbia
France
Lithuania
Denmark
Hungary
Bosnia&Herzegovina
Latvia
Uzbekistan
Turkmenistan
Switzerland
Netherlands
Croatia
Finland
Estonia
Azerbaijan
Sweden
Cyprus
Moldova
Austria
Norway
Luxembourg
Liechtenstein
Iceland
Armenia
Monaco
Contribution, %
Transboundary transport
National emissions

## Slide 15
PAH deposition in 2014
Measurement/Modelling Assessment of PAH pollution, 2014
Transboundary transport of pollution
Inter-annual changes of transboundary fluxes lead to substantial changes of annual deposition in EMEP countries (about 50-70%)
-50%
-25%
0%
25%
50%
75%
100%
Sweden
Norway
Estonia
Finland
Denmark
United Kingdom
Belarus
Latvia
Lithuania
Poland
Slovakia
Italy
Germany
Czech Republic
Austria
Netherlands
France
Belgium
Liechtenstein
Switzerland
Slovenia
Ireland
Changes of PAH deposition from 2013 to 2014

## Slide 16
Exceedance of EU target value for B[a]P (1 ng/m3)
B[a]P air concentrations in 2014
Population in areas with exceeded EU target levels for B[a]P
EMEP measurements: The 95th percentile concentrations exceed 1 ng/m3 at Kosetice (Czech Republic), Waldhof, Zingst (Germany), Rucava (Latvia), and Diabla Gora (Poland)
Modelling: B[a]P air concentrations near or above 1 ng/m3 are calculated for Central and Eastern Europe, and EECCA countries
1 ng/m3 0.6 ng m/3 0.4 ng/m3
Measurement/Modelling Assessment of PAH pollution, 2014

## Slide 17
Evaluation of B[a]P pollution in urban areas
Significant part of population in the EMEP countries lives in areas with exceeded limit values for B[a]P air concentrations
About half of urban/suburban monitoring stations in Europe in 2013 measured B[a]P air concentrations above 1 ng/m3 (EEA, 2015)
A study is initiated to estimate B[a]P pollution levels in urban areas of EMEP countries and provide information for exposure evaluation
Measured B[a]P air concentrations in 2013 (EEA Airbase)
5 x 5 km2
Ostrava
Prague
Modelled B[a]P air concentrations for 2013
Modelling domain

## Slide 18
Measurement/Modeling assessment for 2014
Assessment of pollution for PCDD/Fs, PCBs, and HCB is carried out using multi-scale (global/regional) model simulations
Initial and boundary conditions for evaluation of pollution of EMEP region are generated using global scale modelling with GLEMOS model
For evaluation of global scale transport available emission inventories and data from international organizations are used
To verify global modelling results measurement data from various monitoring networks, databases, and literature are compiled
Global and regional scale modelled PCDD/F air concentrations for 2014
EMEP

## Slide 19
UNEP SC global emissions and measurements of POPs in air and media
PCDD/F emissions of more than 140 countries (based on UNEP Emission Toolkit)
Emission data include PCDD/F releases to air, land, and water
Measurements of PCBs, PCDD/Fs, HCB air concentrations over the globe (SC GMP Data Warehouse)
Annual PCDD/F emissions to air (g I-TEQ/yr)
Measured PCB-153 air concentrations (pg/m3)
Global scale data for evaluation of POP pollution

## Slide 20
Further development of POP modelling approach
Research activities related to regional and global scale modelling:
Refinement of parameterization of atmospheric transformation/removal processes and exchange with media
Further development of source-receptor methodology accounting for multi-media transport of POPs
Analysis of congener composition of emission and concentrations in media (PCDD/Fs, PCBs)
Multi-scale modelling to support transition to the New EMEP grid
Multi-model study of global POP transport applying UNEP SC GMP measurement data
GLEMOS (EMEP/MSC-E)
BETR-Research (Switzerland/Sweden)
Measured and modelled PCB153 in air for the period 2004-2013, pg/m3

## Slide 21
Contribution to the assessment of effectiveness of UNEP SC (Second Global GMP report, 2016)
Co-operation with UNEP Stockholm Convention
Multi-model assessment of global POP pollution and trends
GLEMOS (MSC-E) and BETR (Sweden) models vs. measurements of UNEP SC GMP DWH
EMEP

## Slide 22
Cooperation with international programs (HELCOM and AMAP)
Baltic Sea region
Assessment of atmospheric input of POPs/HMs to Baltic Sea:
Substances – Pb, Cd, Hg, PAHs, PCBs, PCDD/Fs
Deposition maps and source-receptor relationships
Long-term trends (1990-2013)
HELCOM PRESSURE group meeting (Copenhagen, 2016): interest to evaluation of pollution by new substances
Regular pollution assessment over the EMEP domain:
Substances – PAHs, HCB, PCBs, PCDD/Fs
Concentration and deposition maps
Source-receptor relationships
Long-term trends (1990-2014)
AMAP and EMEP domains
EMEP
AMAP
Joint AMAP/CLRTAP workshop (Potsdam, 2016)

## Slide 23
MSC-E work-plan elements for 2017
Operational monitoring and modelling of POP transboundary pollution within EMEP
Model evaluation of POP (B[a]P) contamination of highly populated regions (urban areas)
Evaluation of intercontinental transport and contribution of secondary sources
Refinement of model parameterization of phase partitioning and inter-media exchange of POPs
Contribution to development of emission strategy to improve emissions
Transition of POP operational modelling to the new EMEP grid
Co-operation and exchange of information on POP pollution with subsidiary and international bodies (TFMM, TF HTAP, UNEP, AMAP, HELCOM etc)