## Slide 1
Assessment of POP pollution in EMEP region: current progress and further activities
MSC-E: A. Gusev, V. Shatalov, O. Rozovskaya
CCC: W. Aas, K. Breivik
CEIP: K. Mareckova, S. Poupa, C. Sosa, M. Tista, R. Wankmueller
INERIS: F. Couvidat
5th Joint Session of the EMEP Steering Body and the Working Group on Effects
9-13 September, 2019, Geneva (Switzerland)

## Slide 2
Outcome of activities on POPs in 2019
www.msceast.org
www.ceip.at
www.nilu.no/projects/ccc/
Main topics of Status Report 2/2019:
Detailed results are available in internet:
Emissions of POPs in the EMEP countries (CEIP)
POP monitoring in the EMEP region (CCC)
Model assessment of POP pollution for 2017 (MSC-E)
Contribution to TF TEI work: Levels and trends in B(a)P pollution Population exposure to high B(a)P/PAH levels
Research activities: Case study on B(a)P pollution Refinement of HCB pollution assessment
Co-operation with international organizations
Plans of further activities

## Slide 3
Analysis of B(a)P pollution trends (2007-2017)
Contribution to analysis of the effectiveness of the POP Protocol (TFTEI)
Observed B(a)P pollution levels still exceed EU/WHO limits in many countries
B(a)P air concentrations are increasing in some countries
B(a)P emissions in the EMEP region are almost stable in recent decade
Observed B(a)P levels in air (AIRBASE+EMEP, 2017)
Exceedances of EU/WHO B(a)P limit values in EMEP countries
EU limit
WHO limit
Amount of AIRBASE sites showing decrease/increase of B(a)P levels
Locations of sites with increasing B(a)P levels
B(a)P emissions of EMEP countries

## Slide 4
Population in areas with exceeded EU/WHO limits for B(a)P
1 ng/m3
0.12 ng/m3
B(a)P air concentration (2017)
Human exposure to high B(a)P levels
Contribution to analysis of the effectiveness of POP Protocol (TFTEI)
B(a)P emissions (2017)
~10% of population
~70% of population
Information on exceedances can be delivered to TF Health/WHO PAH group

## Slide 5
Human exposure to mixture of toxic PAHs
PAH compound TEF
Benzo[a]pyrene 1.0
Benzo[b]fluoranthene 0.1
Benzo[k]fluoranthene 0.1
Indeno[1,2,3-c,d]pyrene 0.1
B(a)P equivalent concentrations of 4PAHs:
4PAH (BaPeq) = S PAHi * TEFi
B(a)P-equivalent air concentrations of 4 PAHs for 2017 (ng m-3)
Evaluation of joint toxicity of PAH mixture
List of PAH to considered: POP Protocol – 4 PAHs EU POP Regulation – 8 PAHs US EPA – 16 PAHs
Gas-phase PAHs and toxic PAH derivatives (nitro-PAHs, oxy-PAHs)
Use of B(a)P-toxic equivalent factors (TEF) to predict toxicity of PAH mixture
Joint efforts of TFTEI, EMEP and Parties are needed for further analysis of effectiveness of POP Protocol.
Issues on PAH pollution/exposure are summarized in booklet prepared by MSC-E

## Slide 6
Model sensitivity to major processes
Analysis of model sensitivity to major B(a)P processes:
Key processes: degradation, gas-particle partitioning, air-surface exchange
Largest sensitivity to the model scheme of B(a)P degradation in air
Results of the study will be used to improve model parameterizations of GLEMOS
Co-operation with national experts from France (INERIS)
CHIMERE
B(a)P air concentration (2015)
GLEMOS
Case study on B(a)P pollution in Europe and France (2018-2019)
Research activities on B(a)P pollution
Further activities: 1) multi-model analysis of B(a)P transport (EuroDelta-Carb intercomparison), 2) B(a)P case study for Poland

## Slide 7
Research activities on HCB pollution
Refinement of HCB pollution assessment with focus on secondary sources
Motivation:
HCB is among priority POPs in the Long-term strategy of the Convention (LTS .38)
Slow decline of concentrations, increase at some EMEP sites (last 10 years)
Relative contributions of primary and secondary emissions
Objectives:
Analysis and improvement of HCB model assessment results (MSC-E, CCC)
Development of scenarios of HCB global/historical emissions (JRC, TF HTAP)
Reduction of uncertainties in national HCB emission inventories (TFEIP, Parties)
Measured HCB concentrations (CCC)
EMEP anthropogenic sources
Global anthropogenic sources
Global secondary sources
EMEP secondary sources
HCB air concentration
(model estimates)
Contributions to
?
?

## Slide 8
Ongoing and further activities:
Analysis of model parameterization and refinement of HCB accumulation in media (MSC-E)
Analysis of seasonality of HCB concentrations in 2017 (CCC)
Evaluation of model results using POP Passive Sampling campaign (CCC)
Research activities on HCB pollution
Refinement of HCB pollution assessment with focus on secondary sources
BASE Base case
DEGR Decreased degradation rate in soil
KOW Increased HCB sorption in soil (KOW)
ACCFR Increased accessible fraction of soil for HCB
Experimental model simulations
Effect of primary emissions
HCB
Measurements of HCB in air (2017)
Passive sampling of HCB in air (CCC, preliminary results)
Modelled HCB air concentrations (2016)

## Slide 9
Co-operation with international organizations
Arctic Monitoring and Assessment Programme (AMAP)
  Contribution to the AMAP Assessment of POP Pollution of the Arctic region (2019)
Helsinki Commission (HELCOM)
  Assessment of atmospheric load of HMs and POPs to the Baltic Sea (HMs, PCDD/Fs)
Stockholm Convention (SC)
  Contribution to the SC effectiveness evaluation regional WEOG and Global assessment reports (2019-2021)
European Chemical Agency (EU regulation “Registration, Evaluation, Authorization and Restriction of Chemicals”, REACH)
  Updated EU Regulation on POPs (Regulation 2019/1021)
  ECHA supporting identification of new POPs for listing in the POP Protocol

## Slide 10
Research and model development
  Attribution of long-term changes of POP pollution to regional and extra-regional (global, secondary) sources
  Multi-model analysis of B(a)P pollution using data of 2018 winter period monitoring campaign
National scale pollution assessments (co-operation with countries)
  Initiate studies on B(a)P pollution in Poland and Croatia (2020-2021)
Contribution to the evaluation of effectiveness of POP Protocol (co-operation with TFTEI)
  Analysis of trends and key sources of B(a)P pollution
  Co-operation with Working Group on Effects
  Data exchange with TF Health on B(a)P/PAH concentration and exceedances of target values
  Potential co-operation with JEG-DM on POP cycling and accumulation in the environmental media
  Co-operation with other international organizations
  AMAP, HELCOM, SC
Proposals for bi-annual work-plan (2020/2021)