## Slide 1
Assessment of PAH pollution levels, key sources and trends
A. Gusev, N. Batrakova, V. Shatalov, O. Rozovskaya
24th meeting of the Joint Convention/WHO Task Force on the Health Aspects of Long-range Transboundary Air Pollution, Bonn, Germany (virtual meeting)
10–11 May 2021

## Slide 2
Contribution to analysis of POP Protocol effectiveness in co-operation with TFTEI, TFH (workplan 1.1.1.1)
PAH pollution and population exposure
Long-Term Strategy for the Convention (2020-2030):
“Unintentional releases of PAHs are still a concern”
“Continue scientific research on POP transport and trends with a focus on PAHs”
Main issues considered in the MSC-E report on PAHs:
Trends in B(a)P pollution and exceedances of limit values
Key emission sectors and temporal changes of their contributions
Exposure to mixture of 16 toxic PAHs
Contribution of PAHs to PM adverse effects
Progress Report on PAHs (2020)

## Slide 3
PAH emissions: key sectors and temporal changes
PAH emissions:
Biomass/fossil fuels combustion is the main source of PAHs emission
The largest contribution is made by Residential combustion sector
PAHs are co-emitted with PM from sectors related to combustion
PAH emissions do not change significantly over the past ~20 years
4 PAHs and PM2.5 sectoral emissions (CEIP)
4 PAHs
PM2.5
Chart: 
| Residential Combustion | Industry | Solvents | Agriculture | Road Transport | Other
 | 0.70036 | 0.11694 | 0.065553 | 0.064497 | 0.030381 | 0.16386
Chart: 
| Residential Combustion | Industry | Road Transport | Public Power | Int Shipping | Other
 | 784.6621 | 396.4885 | 189.3178 | 137.9847 | 90.7656 | 370.1815
Chart: B(a)P emission, t/y
| 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018
ResComb | 377.4356 | 376.759 | 366.4277 | 374.2608 | 367.7178 | 370.0119 | 372.9601 | 373.7269 | 383.7879 | 388.2257 | 401.9159 | 384.9874 | 391.0168 | 395.0772 | 374.5793 | 378.4724 | 382.1869 | 379.9043 | 379.8544
Industry | 52.8045 | 53.1309 | 52.2988 | 51.1221 | 52.0246 | 52.3382 | 51.393 | 51.5365 | 50.9586 | 39.1539 | 41.2523 | 42.7689 | 42.1124 | 40.8133 | 40.1216 | 40.4407 | 40.8618 | 43.4664 | 43.327
Agriculture | 50.4618 | 46.1412 | 46.18 | 49.4185 | 45.2152 | 44.488 | 41.8135 | 44.1212 | 45.4993 | 43.8293 | 38.8115 | 40.2777 | 44.1144 | 39.9841 | 36.7034 | 36.5854 | 33.0733 | 31.7836 | 31.7836
Fugitive | 22.0334 | 21.8821 | 21.0076 | 22.2284 | 22.6094 | 20.8123 | 21.7841 | 21.9622 | 21.1983 | 17.6817 | 20.6594 | 20.5588 | 19.3071 | 19.4682 | 19.0977 | 19.2044 | 19.2151 | 19.3668 | 19.2663
Waste | 16.2295 | 18.1489 | 15.6326 | 18.4362 | 16.346 | 14.8923 | 16.2727 | 15.6813 | 15.2204 | 16.3542 | 16.5212 | 16.979 | 13.1292 | 18.8297 | 14.3266 | 16.6769 | 19.8273 | 15.9031 | 15.9031
Other | 18.0141 | 17.0156 | 17.9218 | 18.0972 | 17.9561 | 17.7114 | 17.5765 | 17.7267 | 17.6742 | 18.0975 | 18.4355 | 19.7294 | 20.2405 | 17.35 | 17.4622 | 17.3416 | 17.9236 | 17.7049 | 17.7202

## Slide 4
Chart: CZ0003R
| 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018
Obs | 0.269 | 0.224 | 0.577 | 0.509 | 0.29 | 0.452 | 0.26 | 0.392 | 0.312 | 0.498 | 0.351 | 0.393 | 0.385 | 0.731 | 0.307 | 0.235 | 0.245 | 0.416 | 0.414
Mod | 0.63455 | 0.75305 | 0.65428 | 0.64475 | 0.63879 | 0.53805 | 0.62657 | 0.53454 | 0.52818 | 0.67832 | 0.74008 | 0.62667 | 0.64026 | 0.74842 | 0.62174 | 0.67397 | 0.66954 | 0.68245 | 0.65634
Chart: SE0012R
| 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018
Obs | 0.065 | 0.078 | 0.042 | 0.082 | 0.058 | 0.032 | 0.054 | 0.075 | 0.063 | 0.058 | 0.03 | 0.055 | 0.043 | 0.043 | 0.04 | 0.057 | 0.021 | 0.053 | 0.056
Mod | 0.066769 | 0.052302 | 0.054845 | 0.049701 | 0.057657 | 0.057612 | 0.059813 | 0.069589 | 0.064309 | 0.062546 | 0.037597 | 0.037428 | 0.027858 | 0.029278 | 0.028422 | 0.025675 | 0.022445 | 0.024209 | 0.023728
Long-term changes of B(a)P pollution in the EMEP region
B(a)P concentrations (2018)
Modelled vs measured B(a)P air concentrations at EMEP sites
Modelled B(a)P concentrations generally correspond EMEP measurements
No significant decrease of B(a)P concentrations in modelling results and measurements
EMEP sites with long-term measurements of B(a)P

## Slide 5
Chart: B(a)P in air, ng/m3
| 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018
 | 1.2697 | 0.75947 | 0.69246 | 0.88494 | 0.62567 | 0.61 | 0.47 | 0.67773 | 0.58182 | 0.51537
 | 0.53903 | 0.43921 | 0.91658 | 0.78374 | 0.68762 | 1.1839
 | 1.5127 | 1.1036 | 1.524 | 2.43 | 3.04 | 2.5969 | 2.3687 | 2.1987
 | 0.94241 | 0.96397 | 0.69644 | 0.55106 | 0.81 | 0.64 | 0.82487 | 0.89274 | 1.0495
 | 1.652 | 1.5382 | 1.2644 | 3.3706 | 2.2113 | 2.3182 | 2.7237 | 2.24 | 1.9432 | 1.3404 | 3.9541
 | 3.2667 | 3.0411 | 4.5976 | 1.9176 | 2.13 | 1.78 | 2.8985 | 2.4401 | 1.8489
 | 1.6843 | 1.5243 | 1.34 | 1.34
 | 0.87867 | 0.91977 | 1.3547
 | 8.3132 | 4.1966 | 5.2489 | 5.6051 | 6.2357 | 5.4383 | 6.42 | 4.15 | 3.8473 | 3.7144 | 4.0282
 | 4.3032 | 4.249 | 3.4962
 | 5.1677 | 6.4 | 6.1079 | 4.6482 | 5.25 | 5.0336 | 5.2571 | 3.5248
 | 14.142 | 14.4886 | 10.5353 | 10.5122 | 9.61 | 9.19 | 7.9072 | 6.8729 | 9.2617
Chart: B(a)P in air, ng/m3
| 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018
 | 0.32667 | 0.37215 | 0.42788 | 0.38 | 0.37999 | 0.32977 | 0.29 | 0.333 | 0.35956 | 0.33911 | 0.23233
 | 0.61336 | 0.61558 | 0.92329 | 0.73615 | 0.51759 | 0.56 | 0.54503 | 0.61645 | 0.50574
 | 1.3245 | 1.5434 | 1.1859 | 1.0917 | 1.021 | 1.3222 | 1.0757 | 0.98 | 1.11 | 0.96066 | 1.0758 | 0.6726
 | 0.06088 | 0.10976 | 0.14264 | 0.085 | 0.060437 | 0.06 | 0.061291 | 0.067231 | 0.067056
 | 0.26598 | 0.37903 | 0.46152 | 0.54693 | 0.52194 | 0.3838 | 0.3 | 0.38465 | 0.40862 | 0.19714
 | 0.055706 | 0.09 | 0.084198
 | 0.32848 | 0.38583 | 0.44736
 | 2.451 | 2.2998 | 1.45 | 2.0501 | 2.1045
 | 3.7008 | 2.3175 | 1.95 | 3.18 | 3.6355 | 1.7285 | 1.2401
 | 0.63302 | 0.78612 | 0.679 | 0.79
 | 1.8593 | 1.7826 | 1.66 | 1.2449 | 1.4014 | 1.37 | 1.3244 | 1.4034 | 1.0182
 | 1.9864 | 2.1776 | 2.417 | 1.58 | 2.0928 | 1.9821 | 1.7594
Observed B(a)P concentrations in period 2007-2018 (EU EEA AIRBASE)
Poland
Italy
EU target limit
Implications to the analysis of POP Protocol effectiveness:
Lack of decrease in B(a)P pollution levels and emission during recent ~10-20 years
Exceedances of air quality guidelines are still existed in some of EMEP countries
Long-term changes of B(a)P pollution in the EMEP region
High concentrations near or above air quality guidelines (2018)

## Slide 6
Population in areas with exceeded EU/WHO limits for B(a)P
1 ng/m3
0.12 ng/m3
B(a)P air concentration (2017)
Human exposure to high B(a)P levels
Contribution to analysis of the effectiveness of POP Protocol (TFTEI)
Information on exceedances can be delivered to TF Health/WHO PAH group
B(a)P emissions (2017)
~10% of population
~70% of population

## Slide 7
PAHs are emitted to the atmosphere as a mixture of different compounds
Number of considered PAHs differs in various international organizations and countries
Carcinogenic (CEQ), mutagenic (MEQ), and dioxin-related toxicity (TEQ) equivalents can be estimated for PAH mixture
4 PAHs
BaP, BbF,
BkF, IND
POP Protocol
8 PAHs
BaP, BeP, BaA, DahA, BbF, BjF, BkF, Chry
EU Air Directive/ECHA*
US EPA Priority list
16 PAHs
BaP, BaA, BbF, BkF, DahA, Chry, IND, Acy, Flth, Pyr, Nap, Flu, Ace, BghiP, Ant, Phen
* ECHA – European Chemical Agency
Evaluation of exposure to mixture of toxic PAHs

## Slide 8
Experimental model simulations of 16 PAHs based on expert estimates of emissions (Pekin University project PKU-FUEL, 2015)
B(a)P-equivalent concentrations of 16 PAHs exceed EU target value in many countries
B(a)P equivalent concentrations of 16 PAHs (ng TEQ m-3)
B(a)P equivalent concentrations of 4 PAHs (ng TEQ m-3)
Chart: Contribution. %
| DahA | BbF | BaP | IND | BkF | BaA | NAP | ANTH | BghiP | CHRY | PHEN | ACY | FLU | ACE | FLTH | PYR
 | 39.3205 | 20.1191 | 18.3661 | 5.2578 | 4.9995 | 4.0286 | 2.9751 | 1.4623 | 1.0169 | 0.80027 | 0.63768 | 0.36721 | 0.23894 | 0.20185 | 0.11909 | 0.089015
Contributions of 16 PAHs to total B(a)P equivalent concentrations
Inclusion of additional PAH compounds into the assessment may help to characterize population exposure to toxic PAHs more accurately
Evaluation of exposure to mixture of toxic PAHs
B(a)Peq = S (CPAHi * TEFi)

## Slide 9
Contribution of PAHs to PM adverse effects
PM chemical composition may include:
Air quality assessment for PM is often based on PM mass concentration without considering sources and chemical composition of particles
Impact of PM on human health may be more significant due to the presence of toxic constituents (e.g. PAHs, PCDD/Fs,…)
Analysis of PAH toxicity can contribute to evaluation of adverse effects of PM on human health
Organic components (e.g. PAHs, PCDD/Fs, …)
PM
Heavy metals (e.g. Cd, Pb, …)
Other components
Health effects of PM and PAHs/HMs
Respiratory diseases
Cardiovascular and cardiopulmonary diseases
Carcinogenic and mutagenic effects
…

## Slide 10
Chart: B(a)P, tonnes/year
| 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018
Previous estimate | 70.9314 | 70.3853 | 72.4716 | 50.2536 | 49.7279 | 43.5719 | 45.0698 | 41.5691 | 42.5093 | 44.8526 | 46.2324 | 45.7931 | 44.4352 | 47.3538 | 44.4118 | 44.1979 | 41.5181
Refined estimate | 28.0769 | 26.298 | 29.4587 | 27.0886 | 26.2268 | 27.7666 | 27.6623 | 27.1326 | 29.3161 | 29.7245 | 30.2274 | 25.5681 | 30.8548 | 26.2379 | 28.6916 | 31.7614 | 28.0983 | 27.8239
Research to improve PAH pollution assessment
National scale studies on B(a)P (Spain, France, Poland)
Project domains
Past and on-going studies (2017-2021):
Multi-model study of B(a)P pollution in Spain and France
Analysis and improvement of B(a)P emissions from key sectors (agriculture, domestic heating)
Analysis of model parameterizations for B(a)P
Initiation of a new case study for Poland (2020-2021)
Refinement of B(a)P emissions (Spain):
Updated total emission is 30-60% lower
The dominating sector changed from “Agriculture” to “Residential combustion”
B(a)P emissions in Spain
Previous estimates
Spain
France
Poland
Refined estimates

## Slide 11
Program of the study (2020-2021):
Simulations of B(a)P and other PAH levels in the country involving detailed national data
Model evaluation of updated national PAH emissions inventory and scenarios
Analysis of residential combustion contribution to PAH levels in the country
Estimates of exceedances of the EU and WHO air quality guidelines for PAHs
Inter-comparison of GLEMOS and GEM-AQ model results for B(a)P
Research to improve B(a)P pollution assessment
National scale studies on B(a)P/PAH pollution (Poland)
Observed B(a)P conc (2018) EMEP+AIRBASE
B(a)P, ng m-3
Chart: B(a)P, tonnes/year
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018
PL emission (2019) | 35.8915 | 40.9206 | 40.3769 | 54.4019 | 50.9944 | 51.39 | 50.0991 | 47.6734 | 41.8943 | 41.2611 | 37.3744 | 40.7874 | 42.2297 | 46.3604 | 42.6891 | 41.881 | 44.3966 | 42.8618 | 43.6112 | 40.7976 | 46.1935 | 44.6009 | 46.4585 | 44.9443 | 42.5934 | 43.4094 | 43.5215 | 42.9353
PL emission (2020) | 100.8789 | 126.9399 | 126.4368 | 144.7528 | 124.8607 | 123.4251 | 126.5711 | 108.9529 | 90.125 | 91.845 | 72.6929 | 79.6858 | 86.6947 | 84.4122 | 87.2275 | 93.4588 | 102.4312 | 91.0904 | 94.4215 | 91.8877 | 100.6691 | 86.7322 | 87.4602 | 81.5733 | 72.5233 | 71.5397 | 75.3654 | 74.782 | 73.1881
Long-term changes of B(a)P emissions
Previous inventory
Updated inventory
Spatial distribution of B(a)P emissions
Updated inventory
Previous inventory

## Slide 12
Model domain and B(a)P emissions
Multi-model study of B(a)P pollution
Contribution to EuroDelta-Carb model intercomparison project (TFMM)
Objectives :
Multi-model assessment of B(a)P pollution levels and exceedances of air quality guidelines
Analyzing relationship between B(a)P and PM transport and fate (including PM components – OC, EC)
Contribute to analysis of consistency of residential wood burning emissions
Modeling groups:
Institution | Model | Participants
EMEP/MSC-E | GLEMOS | Alexey Gusev
INERIS (France) | CHIMERE | Augustin Colette
FMI (Finland) | SILAM | Rostislav Kouznetsov, Evegeny Kadantsev
CIEMAT (Spain) | CHIMERE | Marta Garcia Vivanco
ENEA (Italy) | MINNI | Mihaela Mircea, Ilaria Delia, Mario Adani

## Slide 13
Research activities
  Analysis of trends and key sources of PAH pollution in the EMEP region
  Multi-model analysis of B(a)P pollution in 2017/2018 using data of intensive winter monitoring campaign (EuroDelta-Carb)
  Case study on B(a)P pollution in Poland
  Analysis and attribution of long-term changes of PAH pollution on global/regional scale (in co-operation with TF HTAP)
  Co-operation
  Data exchange with TF Health on B(a)P/PAH concentration and exceedances of target values to assess population exposure
  Co-operation with international organizations (HELCOM, …)
Ongoing and further EMEP activities on PAHs